Escom-0.1 -- A Terminal for Embedded Forth Systems

# Preface.
This document describes the escom program.
escom is a terminal program that runs under Windows. It can be used for communicating with an embedded Forth system, like the stm8ef for the STM8 family.

escom is based on e4thcom by Manfred Mahlow. The program was converted to C for Windows compatibility.

For a start, the Forth console can be used to control the embedded system. A simple program like “putty” is sufficient for communication. It is also possible to add new words to the system. But as soon as the first program is written and ready for testing, an easy way to upload the source code files is missing. Simple line editing is also not possible with a standard communication program. A tool to overcome these deficiencies is the escom terminal program.
In terminal mode it sends terminal input without a local echo via serial line to the target (Forth System) and displays characters received from the target in the terminal window.
The escom program can also be used to upload sourcecode to the target system. This can be user written software or readily available library words.
As imbedded system often use symbolic names for the various I/O registers, escom has -just like e4thcom- the capability to make use of these symbolic name in the source code.
# Software package.
escom is written in c as a single source file. The file “escom.c” can be compiled by the gcc compiler that is part of the Strawberry Perl for Windows package. See https://strawberryperl.com for installing the compiler.
The program is tested on a Windows 10 system. An executable “escom.exe” is also supplied.
The command for compiling from source is:
gcc escom.c -o escom
Place the executable (escom.exe) in a directory that is in the PATH environment variable, so it can be started from every directory.
# Using escom.
## Command line options.
Escom can be started with command line options “-d”, “-b “-t” and “-p”. They have the following meaning:

-d COM5 # Serial port for communication with target
-b 115200 # Baudrate for the serial port
-t stm8ef # Target system
-p D:/Forth/stm8ef/mcu;D:/Forth/stm8ef/lib # Search path, separator is ";"

## Options in configuration file.
At startup, escom will try to read options from escom.conf in the user's home directory.
Options on the commandline will overrule the options in the configuration file.
## Search path.
The search path is used for include files if they can not be found in the current directory.
The path definition normally includes the paths that are used for the device specific include files.
For hardware-specific includes for target “stm8ef”, the specification:
\res MCU: STM8S103
in a source file will include the file D:/Forth/stm8ef/mcu/STM8S103.efr in this example.

When including library words the search will include the directory D:/Forth/stm8ef/lib.
For example:
#require ]C!
Will include D:/Forth/stm8ef/lib/]C! If the word does not already exists in the target's dictionary.
## Startup.
When escom starts, it will show the current settings. For example:
C:>escom -d COM3
will show:

escom-0.1 : Serial Terminal for Embedded Forth Systems.
Copyright (C) 2020 Ed Smallenburg. This is free software under the
conditions of the GNU General Public License with ABSOLUTELY NO WARRANTY.

Active options:
-d (PORT ) - COM3
-b (BAUDRATE) - 115200
-t (TARGET ) - stm8ef
-p (PATH ) - D:/Forth/stm8ef/mcu;D:/Forth/stm8ef/lib
======================================================================================

Followed by the “ok” prompt of the target Forth system if all works well.
# Program example.
In the “examples” directory there are some example Forth programs. The neotest.fs program drives a neopixel string with various patterns. It includes some machine code to drive the neopixels at the required bit rate. At the beginning of the program code you will see the lines:
\ neotest.fs
\ Testing neopixels on D4
\ 14-12-2020, Ed Smallenburg
\ Protocol:
\ Per pixel 8 bytes are sent. The order is Green, Red, Blue. The most significant
\ bit is the first to be send.
\ "0" bits are sent as 375 nsec high followed by 938 nsec low.
\ "1" bits are sent as 750 nsec high followed by 438 nsec low.
#require ]C!
#require ]B!
\res MCU: STM8S103
\res export PD_ODR PD_DDR PD_CR1 PD_CR2

This program can be sent to the STM8S103 target by the command:
#include neotest.fs
The first 8 lines are comments, they all start with <backslash><space>. These lines will not be sent to the target, but will be shown on the console.
The next 2 lines starts with “#require”. escom will check if the words (“]C!” and “]B!” in this example) are already available in the target system. If not, the file (with the same name as the word) will be uploaded to the target system.
The next 2 lines of the source code start with “\res”.
The first line (“\res MCU: STM8S103”) will read the hardware definition for the STM8S103 cpu to make them available to be accessed by their symbolic names. Nothing will be uploaded to the target at this stage.
The second line exports some of the hardware related symbols to the target as CONSTANTs, so the rest of the program may refer to the symbolic names.
Normally these CONSTANTs are added to the RAM dictionary as they are only needed at compile time, but they can be stored in the NVM dictionary if you want to be able to access then after a cold start.